## Slide 1
Parallel Mandelbrot
Set Renderer
Master-Worker Dynamic Scheduling with MPI
Sean Balbale
CPSC 375: High-Performance Computing
Instructor: Peter Yoon · April 26, 2026
Three Idiots Cluster · 24 MPI Processes
Notes: Welcome. This is the 10-minute presentation for CPSC 375 Term Project. The goal: present the parallel Mandelbrot renderer using MPI master-worker dynamic scheduling, and explain what the scaling data means.

## Slide 2
Motivation: Why Parallelize Mandelbrot?
4096 × 4096, Nmax = 1000
O(N³)
Embarrassingly Parallel
Each pixel is independent — no data dependencies across the image. Perfect for distributed-memory parallelism.
≈100×
Load Imbalance Problem
Boundary pixels iterate up to Nmax steps; interior/exterior pixels escape in 1–5. Row cost varies by 100×.
Dynamic
Solution: Work-Pool Dispatch
Master distributes one row at a time to idle workers — naturally absorbs imbalance with no a priori knowledge.
Notes: Mandelbrot is perfectly parallel at the pixel level — but row-level load imbalance kills static decomposition. Dynamic scheduling is the right answer.

## Slide 3
Architecture: Master-Worker Dynamic Scheduling
RANK 0
MASTER
① Seed workers with first rows
② MPI_Recv any result
③ memcpy row to image buffer
④ Dispatch next row (or TAG_DONE)
⑤ Write PPM after all rows done
RANK 1 · WORKER
Recv row → escape() loop
→ Send results back
RANK 2 · WORKER
Recv row → escape() loop
→ Send results back
RANK 3 · WORKER
Recv row → escape() loop
→ Send results back
· · · Ranks 4–23
TAG_WORK (row idx)
TAG_RESULT (row | iters[W])
TAG_DONE (retire)
Message Sizes · TAG_WORK: 1 INT · TAG_RESULT: (W+1) INTs · 4096-wide → ≈16 KB/row
Notes: Walk through the protocol: seed, receive loop, retire. Emphasize that rank 0 does ZERO pixel computation — pure orchestration. This is why we normalize efficiency by P-1.

## Slide 4
Core Computation & Build Environment
escape() — inner computation kernel
static inline int escape(double cr, double ci,
int max_iter) {
double zr = 0.0, zi = 0.0;
for (int n = 0; n < max_iter; n++) {
double zr2 = zr * zr; // cached
double zi2 = zi * zi; // cached
if (zr2 + zi2 > 4.0) return n;
zi = 2.0 * zr * zi + ci;
zr = zr2 - zi2 + cr;
}
return max_iter;
}
Cached squares
zr² and zi² computed once per iteration — saves 2 multiplications. At Nmax=1000, that's 2,000 fewer flops per boundary pixel.
-O3 -xHost compiler flags
Intel mpiicx enables AVX2/AVX-512 auto-vectorization. Per-column escape() is unrolled and SIMD-accelerated.
Row granularity
One row per work unit keeps the work-pool fine-grained relative to row compute cost — eliminates essentially all load imbalance.
MPI_Wtime() bracketing
Timer starts after initial seeding, stops before PPM write. Measures the computation + communication kernel only.
Notes: The -O3 -xHost flags matter: xHost enables AVX2/AVX-512 vectorization on each node, which is why the escape loop is so fast. Caching zr2 and zi2 saves 2 multiplications per iteration — at 1000 iterations per pixel that adds up.

## Slide 5
Experimental Setup — Three Idiots Cluster
NODE 0 (Master Host)
M
W
W
W
W
W
W
W
NODE 1
W
W
W
W
W
W
W
W
NODE 2
W
W
W
W
W
W
W
W
Strong Scaling
Weak Scaling
Problem Sizes
1024², 2048², 4096² (Nmax=1000)
512² base tile → (512·⌊√P⌋)²
Process Range
P = 2 … 24
P = 2 … 24
Trials / Statistic
3 trials each → median wall time
3 trials each → median wall time
Timer
MPI_Wtime() (compute + comm only)
MPI_Wtime() (compute + comm only)
Notes: Three nodes, 8 cores each, joined over 10GbE TCP. The TCP fabric matters — each 4096-wide result message is 16 KB. At 23 workers sending simultaneously, that's 368 KB bursting at the master. This is why efficiency drops at high P for the large problem.

## Slide 6
Strong Scaling — Speedup S(P) = T(2) / T(P)
Chart: 
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24
1024×1024 | 1 | 3.871 | 5.632 | 8.104 | 10.558 | 12.131 | 13.94 | 16.298 | 17.254 | 18.478 | 20.301 | 20.641
2048×2048 | 1 | 3.475 | 5.477 | 7.847 | 9.933 | 11.687 | 13.589 | 15.627 | 16.759 | 18.698 | 20.682 | 21.046
4096×4096 | 1 | 3.331 | 5.265 | 7.356 | 9.256 | 10.83 | 12.433 | 14.06 | 15.554 | 16.948 | 18.533 | 19.647
Ideal (P−1) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23
20.6×
P=24 · 1024² · E=0.897
21.0×
P=24 · 2048² · E=0.915
8.10×
P=8 · 1024² · Super-linear
E=1.16
Notes: The 1024 and 2048 lines both track above the ideal line at moderate P — that's the super-linear speedup. Larger problem = slower at P=2 because image buffer doesn't fit in cache; but it also means more room to grow. The 4096 line stays below ideal, which makes sense — 16 KB result messages dominate.

## Slide 7
Super-Linear Speedup: Cache Amplification Effect
P = 2 (1 worker)
Image buffer: 1024² × 4B = 4 MB → Overflows L2 cache → RAM reads dominate
P = 8 (7 workers, ~146 rows each)
Per-worker share: 146 rows × 4B × 1024 = 598 KB → Fits in L2 cache → Zero RAM latency
While cache amplification appears to violate Amdahl's law, it has a well-established physical explanation: each additional worker reduces per-worker working-set size until it fits entirely inside L1/L2 cache — eliminating memory-latency stalls in the escape() inner loop.
1.16×
Efficiency at P=8
(1024² problem)
1.05×
Efficiency at P=8
(4096² problem)
16%
Super-linear
bonus from cache
Notes: This is the most interesting result. At P=2, the single worker's image buffer for 1024x1024 is 4 MB — way bigger than L2 cache. At P=8, each worker handles ~128 rows; that's only 512 KB. The data fits in cache and iteration becomes memory-latency-free. That's 16% extra speedup from cache effects alone.

## Slide 8
Weak Scaling — Normalized Time T(P) / T(2)
Chart: 
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Measured T(P)/T(2) | 1 | 0.509 | 0.773 | 0.652 | 0.543 | 0.419 | 0.368 | 0.703 | 0.612 | 0.562 | 0.524 | 0.48 | 0.446 | 0.425 | 0.651 | 0.631 | 0.602 | 0.564 | 0.543 | 0.526 | 0.503 | 0.486 | 0.486
Ideal = 1.0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0.37×
Min normalized
time (P=8, tier 2)
<1.0
Every single
measurement
3 tiers
512² → 1024²
→ 1536² → 2048²
Notes: The sawtooth is not a bug — it's the tile design. Within each tier, adding workers reduces per-worker rows without growing the problem; cache efficiency improves and wall time falls. At tier boundaries (P=4, 9, 16) the problem jumps and time resets toward 1.0. Every normalized time is below 1.0 — better-than-ideal weak scaling.

## Slide 9
Amdahl's Law Fit — How Much is Serial?
S(P) = 1 / ( f + (1−f) / P )
Problem Size | Serial Fraction f | Theoretical Max S | S(24) Measured
1024 × 1024 | 0.71% | ≈ 141× | 20.6×
2048 × 2048 | 0.61% | ≈ 164× | 21.0×
4096 × 4096 | 0.96% | ≈ 104× | 19.6×
What limits efficiency at P=24?
Rank 0's single-threaded dispatch loop serializes 23 worker results over TCP. With 4096-wide rows, each recv handles 16 KB; the master becomes a bottleneck.
Why is f smallest for 2048²?
The master's sequential overhead — O(height) dispatch operations — is fixed per row. Wider rows (more flops/row) dilute the serial fraction; 2048 hits the sweet spot.
What does this imply for scaling?
With f < 1%, the implementation could theoretically scale to 100+ workers. The Three Idiots cluster is the binding constraint — not the algorithm.
Notes: All three serial fractions are below 1%. That means rank 0's dispatch loop — which runs in O(height) sequential operations — accounts for less than 1% of total runtime. The theoretical ceiling is ~100–164×, well beyond the 23-worker hardware ceiling. The bottleneck is not the algorithm; it is the cluster size.

## Slide 10
Key Findings
20–21×
Speedup at P=24 across all three problem sizes — worker efficiency stays above 0.85 throughout.
E > 1.0
Super-linear speedup for P ≤ 16 (1024² and 2048²), driven by cache amplification as per-worker working set shrinks.
f < 1%
Amdahl serial fraction below 1% for all sizes — theoretical ceiling of 100–164×, well beyond the hardware limit.
< Ideal
Weak scaling consistently better than ideal — cache gains within each tier outpace the tile-size growth at boundaries.
Future Work: Replace single-master dispatch with distributed work-stealing to eliminate the rank-0 bottleneck and scale to 100+ processes.